ACC770 Industrial UHF Handheld Reader

Product Name: ACC770 Industrial PDA UHF Handheld Reader

Product Details:

| RFID |  |
| --- | --- |
| Type | Industrial PDA UHF Handheld Reader |
| Operating Frequency | UHF(Ultra High Frequency) 860~960MHz (software controlled) |
| Protocol | ISO18000-6C, EPC UHF Class 1 Gen 2 |
| Reading Range | 70 ~ 120cm ( 4 feet maximum ) |
| Antenna Polarization | Circular Polarized |
| RF Power | 1 Watt |
| SDK | SDK provided with Reader |
| System features |  |
| Operating system | Microsoft® Windows CE® 5.0 Professional |
| Processor | Samsung Processor 400MHz |
| Memory |  |
| Memory | 128 MB SDRAM, 1GB Max. |
| Flash memory | 128 MB Flash ROM |
| Audio, Slots, and Ports |  |
| USB Ports | 1 USB Interface |
| Slots | 1 MicroSD Slot |
| Input/Output devices |  |
| Input devices | 26 key keyboard, Touch screen, stylus, Button Trigger |
| Output devices | 3.5” Transmissive LCD, 320 x 240 pixels, LED x 2, Buzzer |
| Communication features |  |
| WiFi | 802.11b/g |
| Bluetooth | Bluetooth 2.0 |
| GPRS |  |
| Product specifications |  |
| Dimensions | 186 x 75 x 31 mm (w x d x h) |
| Weight | 400g |
| Energy Efficiency |  |
| Battery | Removable, rechargeable, powerful 4400 mAh battery |
| Power supply | AC Adapter |
| Environment Requirement |  |
| Case Protection | IP64 |
| Operating Temp | -20°C to 50°C (-4°F to 122°F) |
| Storage Temp | -40°C to 75°C (-40°F to 167°F) |
| Humidity | 5% to 95% Non-condensing |

ACC Systems Inc.  1 Robert Lane,  Glen Head, NY 11545  ph. 516-674-0191

Email: rfid@accsystemsinc.com   web: www.accsystemsinc.com